M3315/CSE3365
Spring 2015
Project 2 – Rootfinding
Due 4pm Tue, Feb 24, 2015

The characteristic function of a dielectric slab waveguide (look it up in wikipedia!)
is rather complicated. It is given by,

ital{f}(%beta,%omega) = ital{cos}(%alpha_1)(%alpha_1 - {%alpha_1}{%alpha_0}) + ital{sin}(%alpha_1)({%alpha_1}^2 - {%alpha_0}^2) ,
where,
%alpha_0 = sqrt{%beta^2 - ital{n_0}^2%omega^2}

%alpha_1 = sqrt{ital{n_1}^2%omega^2 - %beta^2}

and n0, n1 are refractive indices, ω is the frequency of the guided wave and β is the propagation constant. To determine which light waves are guided by the waveguide, an engineer has to solve the equation
ital{f}(%beta, %omega) = 0 ,

for β, where ω is the given parameter, and the refractive indices are fixed. In our example, we set n0 = 1 and n1 = 2 and try out different values of ω. From the definition of the α's it is clear that we can compute real f(β, ω) only for β in the interval [n0 ω, n1ω].

Part 1. Write a subroutine

function y = fcn(beta, omega)

that computes the characteristic function for the given values of n0 = 1 and n1 = 2. It should compute the α's as intermediate results and then evaluate the function as it is written here. To get a picture of how the graph of the function looks, create a plot in matlab as follows

omega = 1.0;
beta = omega * linspace(1, 2, 500);
for I = 1 : 500
  y(i) = fcn(beta(i), omega);
end
plot(beta, y);

If you see exactly one root between 1.56 and 1.57 then your function is probably right, otherwise go back and check your code.

Part 2. Now we want to find the exact root of the characteristic function. To that end, modify the function bisect.m in Blackboard. The interface should have the form

[c, res] = p2bisect(a, b, N, omega);

where a, b, c, N are as usual, omega is the frequency (which will be passed to the function) and res = abs(fcn(c, omega)) is the residual of the final root. You should also change function calls fcn(x) to fcn(x, omega) and remove the function fcn at the bottom of the file. Then matlab will execute the code in the file fcn.m which you wrote for Part 1. Use the modified bisect.m to compute the root. Start with the interval a = 1.5, b = 1.6. Use the formula given in class to determine the number of iterations that ensure the error of the root is at most abs{ital{c}_k - %beta} < 10^{-12} . Note that we still have omega = 1. Display the root, the number of iterations and the residual.

Part 3. Re-do Part 1. with omega = 8. How many roots do you see on the graph? For each root, pick an interval of length 1 that contains the root, by visually inspecting the graph of the function. Then compute each root with the bisection method as in Part 2.

Part 4. Implement the regula false method. You can start out with your bisect.m file (i.e., copy it to regulafalsi.m and do the modifications). The interface should be

function [c, N, res] = regulafalsi(a, b, epsilon, omega)

where c, a, b, omega, res are as before, epsilon is the stopping criterium and N is the number of iterations. That is, the iteration should stop when abs(yc) < epsilon. Recompute the roots in Part 3 with the regula falsi method using the same initial intervals. Does the regula falsi need fewer iterations than the bisection method?

Part 5. Re-do Part 4 with the only difference being that the stopping criterium is epsilon = 1e-15. Are the results what you expected? Explain what happened.

The completed project comprises of:
- A project script and the functions fcn.m, bisect.m, and regulafalsi.m, which must be submitted to Blackboard under Assignments → Project 2.
- A printout of the html-published m-script that shows the code, the figures, and your answers as comments. The script should be grouped into cells. One cell for each part. The print out can be either turned in before class or placed by the due date in Prof. Tausch's mailbox in Clements 208.

Please be aware that the presentation of your work will affect your grade. In particular, write whole sentences, format numeric output, annotate the figures, and use a staple.